## Slide 1
Horse Hill: Is the Kimmeridge a game changer?
UK Oil & Gas Investments PLC

## Slide 2: Oil and Gas Accumulations: Types
Source: USA EIA and UKOOG

## Slide 3: Weald & IoW Basin: UKOG interests, Fields,Wells
IoW P1916
IoW 14th Round
Application
Horse Hill Field PEDL 137/246 140 km sq (36000 acres)
Brockham Field
Horndean and Markwells Wood Fields
Baxters Copse Discovery
Brockham Field
Source: DECC, UKOG, ESRI
Grey=BGS shale potential area

## Slide 4: Weald Basin Creaming Curve
Horse Hill: typical Weald conventional field – Bread & Butter
Biggest Portland Sandstone field 5-12+ Million bbl OIIP
Step change needs new play concept i.e. Triassic, Kimmeridge
Source: BGS and UKOG
Horse Hill 2014
UKOG Field Interest

## Slide 5: Horse Hill U. Portland Field: Bread & Butter
HH-1
CF-1
Lowest Known Oil 1900 ft tvdss
Maximum Closure
~1960-1980ft
Source: UKOG

## Slide 6: Distribution of Kimmeridge Clay (“KC”)
KC Lies immediately below Portland and time equivalent rocks
N. Sea- World Class source rock- generated 2 trillion bboe, discovered 50 billion bbl
Current Weald Paradigm: rich source rock not cooked enough to generate much oil/gas except in w. basin centre
Green - offshore Central & Viking Graben Systems
Purple – onshore Weald, Wessex & IoW
Red – Oil and gas fields
Source: Kimmeridge Energy, UKOG
Horse Hill
KC
UKOG IoW
KC

## Slide 7: Kimmeridge at Dorset Coast
Source: Celtique Energy

## Slide 8: Kimmeridge Micrite: Hybrid Oil Play
@3000 ft MD 5.83% TOC,
S241mgHC/g
HI 699
Horse Hill: 1500 ft gross KC
2 limestones with porosity c. 100 ft gross thick
Encased in highly organic rich thermally mature source rock
Oil saturations in upper limestone
Balcombe oil generated from KC
Source: UKOG, Bryneich

## Slide 9: HH KC Geochemistry vs BGS 2014
HH KC - very rich source rock particularly in middle section between limestone reservoir units
TOC 4.64-9.4%, 2715-3345 ft tvdss encasing limestones
Generative Potentials V. High 45-103 kg/tonne
Source: BGS 2014, UKOG
HH Kimmeridge Clay Sample Analyses
BGS 2014 Weald Shale report data

## Slide 10: HH Kimmeridge is Different to N. Sea/Wessex – major impact on source maturity modelling
W. Africa/Brazil, E & C African Rifts, S. Atlantic
Kimmeridge N. Sea, Lias Wessex basin
(Carboniferous Coal
Measures SNS)
Source: BGS 2014, UKOG
HH Kimmeridge Clay Sample Analyses HI 759-1098

## Slide 11: KC Thermal Maturity post HH-1
Source rock: sedimentary rock rich in organic matter which, if subjected to sufficient heat and pressure over geological time, will generate oil or gas.
Normally >1-2% organic matter (TOC)
Thermally mature: source rocks which have received sufficient temperature and pressure over geological time to generate hydrocarbons (defined as vitrinite reflectance (Ro) >0.5%)
Source: UKOG, NuTech
HH Kimmeridge Clay Ro 0.62-.81
BGS 2014 Ro <0.6

## Slide 12: HH-1 KC Thermal Maturity vs BGS 2014
Source: BGS 2014, UKOG
HH-1: ~1300 gross ft of thermally mature Kimmeridge Clay organic rich shale Within early to peak oil generation window
Horse Hill changes the current KC Paradigm

## Slide 13: UKOG Horse Hill: What Next?
Source: Kimmeridge Energy
Proof of Concept
Complete Geochemical Analyses
Nutech electric log, rock mechanics and OIIP analyses
Well trade for Balcombe core data
HH Flow test
  Presence of natural fractures ?
Determine whether:
  KC oil limit defined by an oil water contact (i.e. conventional trap) or
  Ubiquitous where KC limestone porosity lies within mature KC source rock (i.e. hybrid play)
  KC Shale potential (i.e. unconventional)
Economic viability

## Slide 14: Kimmeridge Could Make a Difference!
UK vs. USA Oil Production
Source: Kimmeridge Energy